## Slide 1: University of South Florida Basic Laser Safety Training

## Slide 2: Part 1: Fundamentals of Laser Operation

## Slide 3: Laser Fundamentals
The light emitted from a laser is monochromatic, that is, it is of one color/wavelength. In contrast, ordinary white light is a combination of many colors (or wavelengths) of light.
Lasers emit light that is highly directional, that is, laser light is emitted as a relatively narrow beam in a specific direction. Ordinary light, such as from a light bulb, is emitted in many directions away from the source.
The light from a laser is said to be coherent, which means that the wavelengths of the laser light are in phase in space and time. Ordinary light can be a mixture of many wavelengths.
These three properties of laser light are what can make it more hazardous than ordinary light. Laser light can deposit a lot of energy within a small area.

## Slide 4: Incandescent vs. Laser Light
Many wavelengths
Multidirectional
Incoherent
Monochromatic
Directional
Coherent

## Slide 5: Common Components of all Lasers
Active Medium
The active medium may be solid crystals such as ruby or Nd:YAG, liquid dyes, gases like CO2 or Helium/Neon, or semiconductors such as GaAs. Active mediums contain atoms whose electrons may be excited to a metastable energy level by an energy source.
Excitation Mechanism
Excitation mechanisms pump energy into the active medium by one or more of three basic methods; optical, electrical or chemical.
High Reflectance Mirror
A mirror which reflects essentially 100% of the laser light.
Partially Transmissive Mirror
A mirror which reflects less than 100% of the laser light and transmits the remainder.

## Slide 6: Laser Components
Gas lasers consist of a gas filled tube placed in the laser cavity. A voltage (the external pump source) is applied to the tube to excite the atoms in the gas to a population inversion. The light emitted from this type of laser is normally continuous wave (CW).

## Slide 7: Lasing Action
Energy is applied to a medium raising electrons to an unstable energy level.
These atoms spontaneously decay to a relatively long-lived, lower energy, metastable state.
A population inversion is achieved when the majority of atoms have reached this metastable state.
Lasing action occurs when an electron spontaneously returns to its ground state and produces a photon.
If the energy from this photon is of the precise wavelength, it will stimulate the production of another photon of the same wavelength and resulting in a cascading effect.
The highly reflective mirror and partially reflective mirror continue the reaction by directing photons back through the medium along the long axis of the laser.
The partially reflective mirror allows the transmission of a small amount of coherent radiation that we observe as the “beam”.
Laser radiation will continue as long as energy is applied to the lasing medium.

## Slide 8: Lasing Action Diagram
Energy Introduction
Ground State
Excited State
Metastable State
Spontaneous Energy Emission
Stimulated Emission of Radiation

## Slide 10: WAVELENGTHS OF MOST COMMON LASERS
Argon fluoride (Excimer-UV) Krypton chloride (Excimer-UV) Krypton fluoride (Excimer-UV) Xenon chloride (Excimer-UV) Xenon fluoride (Excimer-UV) Helium cadmium (UV) Nitrogen (UV) Helium cadmium (violet) Krypton (blue) Argon (blue) Copper vapor (green) Argon (green) Krypton (green) Frequency doubled Nd YAG (green) Helium neon (green) Krypton (yellow) Copper vapor (yellow)
0.193 0.222 0.248 0.308 0.351 0.325 0.337 0.441 0.476 0.488 0.510 0.514 0.528 0.532 0.543 0.568 0.570
Helium neon (yellow) Helium neon (orange) Gold vapor (red) Helium neon (red) Krypton (red) Rohodamine 6G dye (tunable) Ruby (CrAlO3) (red) Gallium arsenide (diode-NIR) Nd:YAG (NIR) Helium neon (NIR) Erbium (NIR) Helium neon (NIR) Hydrogen fluoride (NIR) Carbon dioxide (FIR) Carbon dioxide (FIR)
0.594 0.610 0.627 0.633 0.647 0.570-0.650 0.694 0.840 1.064 1.15 1.504 3.39 2.70 9.6 10.6
Key: UV = ultraviolet (0.200-0.400 µm) VIS = visible (0.400-0.700 µm) NIR = near infrared (0.700-1.400 µm)
Wavelength (mm)
Laser Type

## Slide 11: Laser Output
Continuous Output (CW)
Pulsed Output (P)
watt (W) - Unit of power or radiant flux (1 watt = 1 joule per second).
Joule (J) - A unit of energy
Energy (Q) The capacity for doing work. Energy content is commonly used to characterize the output from pulsed lasers and is generally expressed in Joules (J).
Irradiance (E) - Power per unit area, expressed in watts per square centimeter.
Energy (Watts)
Time
Energy (Joules)
Time

## Slide 12: Part 2: Laser Hazards

## Slide 13: Types of Laser Hazards
Eye : Acute exposure of the eye to lasers of certain wavelengths and power can cause corneal or retinal burns (or both). Chronic exposure to excessive levels may cause corneal or lenticular opacities (cataracts) or retinal injury.
Skin : Acute exposure to high levels of optical radiation may cause skin burns; while carcinogenesis may occur for ultraviolet wavelengths (290-320 nm).
Chemical : Some lasers require hazardous or toxic substances to operate (i.e., chemical dye, Excimer lasers).
Electrical : Most lasers utilize high voltages that can be lethal.
Fire : The solvents used in dye lasers are flammable. High voltage pulse or flash lamps may cause ignition. Flammable materials may be ignited by direct beams or specular reflections from high power continuous wave (CW) infrared lasers.

## Slide 14: Lasers and Eyes
What are the effects of laser energy on the eye?
  Laser light in the visible to near infrared spectrum (i.e., 400 - 1400 nm) can cause damage to the retina resulting in scotoma (blind spot in the fovea). This wave band is also know as the "retinal hazard region".
  Laser light in the ultraviolet (290 - 400 nm) or far infrared (1400 - 10,600 nm) spectrum can cause damage to the cornea and/or to the lens.
Photoacoustic retinal damage may be associated with an audible "pop" at the time of exposure. Visual disorientation due to retinal damage may not be apparent to the operator until considerable thermal damage has occurred.

## Slide 15: Symptoms of Laser Eye Injuries
Exposure to the invisible carbon dioxide laser beam (10,600 nm) can be detected by a burning pain at the site of exposure on the cornea or sclera.
Exposure to a visible laser beam can be detected by a bright color flash of the emitted wavelength and an after-image of its complementary color (e.g., a green 532 nm laser light would produce a green flash followed by a red after-image).
The site of damage depends on the wavelength of the incident or reflected laser beam:
When the retina is affected, there may be difficulty in detecting blue or green colors secondary to cone damage, and pigmentation of the retina may be detected.
Exposure to the Q-switched Nd:YAG laser beam (1064 nm) is especially hazardous and may initially go undetected because the beam is invisible and the retina lacks pain sensory nerves.

## Slide 16: Skin Hazards
Exposure of the skin to high power laser beams (1 or more watts) can cause burns. At the under five watt level, the heat from the laser beam will cause a flinch reaction before any serious damage occurs. The sensation is similar to touching any hot object, you tend to pull your hand away or drop it before any major damage occurs.
With higher power lasers, a burn can occur even though the flinch reaction may rapidly pull the affected skin out of the beam. These burns can be quite painful as the affected skin can be cooked, and forms a hard lesion that takes considerable time to heal.
Ultraviolet laser wavelengths may also lead to skin carcinogenesis.

## Slide 17: Other Hazards Associated with Lasers
Chemical Hazards
  Some materials used in lasers (i.e., excimer, dye and chemical lasers) may be hazardous and/or contain toxic substances. In addition, laser induced reactions can release hazardous particulate and gaseous products.
  (Fluorine gas tanks)
Electrical Hazards
  Lethal electrical hazards may be
  present in all lasers, particularly
  in high-power laser systems.
Secondary Hazards including:
  cryogenic coolant hazards
  excessive noise from very high energy lasers
  X radiation from faulty high-voltage (>15kV) power supplies
  explosions from faulty optical pumps and lamps
  fire hazards

## Slide 18: Part 3: Classification of Lasers and Laser Systems

## Slide 19: Laser Safety Standards and Hazard Classification
Lasers are classified by hazard potential based upon their optical emission.
Necessary control measures are determined by these classifications.
In this manner, unnecessary restrictions are not placed on the use of many lasers which are engineered to assure safety.
In the U.S., laser classifications are based on American National Standards Institute’s (ANSI) Z136.1 Safe Use of Lasers.

## Slide 20: Laser Class
The following criteria are used to classify lasers:
Wavelength. If the laser is designed to emit multiple wavelengths the classification is based on the most hazardous wavelength.
For continuous wave (CW) or repetitively pulsed lasers the average power output (Watts) and limiting exposure time inherent in the design are considered.
For pulsed lasers the total energy per pulse (Joule), pulse duration, pulse repetition frequency and emergent beam radiant exposure are considered.

## Slide 21: ANSI Classifications
  Class 1 denotes laser or laser systems that do not, under normal operating conditions, pose a hazard.
  Class 2 denotes low-power visible lasers or laser system which, because of the normal human aversion response (i.e., blinking, eye movement, etc.), do not normally present a hazard, but may present some potential for hazard if viewed directly for extended periods of time (like many conventional light sources).

## Slide 22: ANSI Classifications (cont’d)
  Class 3a denotes some lasers or laser systems having a CAUTION label that normally would not injure the eye if viewed for only momentary periods (within the aversion response period) with the unaided eye, but may present a greater hazard if viewed using collecting optics. Class 3a lasers have DANGER labels and are capable of exceeding permissible exposure levels. If operated with care Class 3a lasers pose a low risk of injury.
  Class 3b denotes lasers or laser systems that can produce a hazard it viewed directly. This includes intrabeam viewing of specular reflections. Normally, Class 3b lasers will not produce a hazardous diffuse reflection.
  Class 4 denotes lasers and laser systems that produce a hazard not only from direct or specular reflections, but may also produce significant skin hazards as well as fire hazards.

## Slide 23: Hazard Evaluation- Reflections
Specular reflections are mirror-like reflections and can reflect close to 100% of the incident light. Flat surfaces will not change a fixed beam diameter only the direction. Convex surfaces will cause beam spreading, and concave surfaces will make the beam converge.
Diffuse reflections result when surface irregularities scatter light in all directions. The specular nature of a surface is dependent upon the wavelength of incident radiation. A specular surface is one that has a surface roughness less than the wavelength of the incident light. A very rough surface is not specular to visible light but might be to IR radiation of 10.6 µm from a CO2 laser.

## Slide 24: Reflection Hazards (cont’d)
Specular Reflection
Diffuse Reflection

## Slide 25: Hazard Terms
Maximum Permissible Exposure (MPE)
The MPE is defined in ANSI Z-136.1"The level of laser radiation to which a person may be exposed without hazardous effect or adverse biological changes in the eye or skin."
The MPE is not a distinct line between safe and hazardous exposures. Instead they are general maximum levels, to which various experts agree should be occupationally safe for repeated exposures.
The MPE, expressed in [J/cm^2] or [W/cm^2], depends on the laser parameters:
wavelength,
exposure duration,
pulse Repetition Frequency (PRF),
nature of the exposure (specular, diffuse reflection).

## Slide 26: Hazard Terms (cont’d)
Nominal Hazard Zone (NHZ)
In some applications open beams are required, making it necessary to define an area of potentially hazardous laser radiation.
This area is called the nominal hazard zone (NHZ) which is defined as a space within which the level of direct, scattered, or reflected laser radiation exceeds the MPE.
The purpose of a NHZ is to define an area in which control measures are required.

## Slide 27: Part 4: Control Measures and Personal Protective Equipment

## Slide 28: CONTROL MEASURES
Engineering Controls
  Interlocks
  Enclosed beam
Administrative Controls
  Standard Operating Procedures (SOPs)
  Training
Personnel Protective Equipment (PPE)
  Eye protection

## Slide 29: Laser Protective Eyewear Requirements
Laser Protective eyewear is to be available and worn in by all personnel within the Nominal Hazard Zone (NHZ) of Class 3 b and Class 4 lasers where the exposures above the Maximum Permissible Exposure (MPE) can occur.
The attenuation factor (optical density) of the laser protective eyewear at each laser wavelength should be specified by the Laser Safety Officer (LSO).
All laser protective eyewear shall be clearly labeled with the optical density and the wavelength for which protection is afforded. This is especially important in areas where multiple lasers are housed.
Laser protective eyewear shall be inspected for damage prior to use.
Optical Density (OD)
The OD (absorbance) is used in the determination of the appropriate eye protection. OD is a logarithmic function.

## Slide 30: Common Laser Signs and Labels

## Slide 31: Laser Safety Contact Information
Adam Weaver, CHP
Laser Safety Officer
MDC Box 35
(813) 974-1194
aweaver@research.usf.edu
Division of Research Compliance
(813) 974-5638
(813) 974-7091 (fax)